SECTION 01 35 29

SAFETY AND HEALTH ON WLSSD PROJECTS

PART 1	GENERAL

1.01	DESCRIPTION OF WORK

A.	Initiate, maintain, and supervise safety and health precautions and programs in connection with the work as specified in the Contract Documents. Take necessary precautions for the safety of, and provide the necessary protection to prevent damage, injury or loss to persons on the work site or those who may be affected by the work.

1.02	RELATED WORK ELSEWHERE [MODIFY THE FOLLOWING ACCORDING TO THE REQUIREMENTS OF THE SPECIFIC PROJECT. CHANGE LETTERING ACCORDINGLY]

- Submittals are delineated in Section 01 33 00 – SUBMITTALS.

- The Planning Document is defined in:

Section 33 01 30.16 – CCTV INSPECTION OF SEWER PIPELINES

Section 33 01 30.17 – MULTI-SENSOR ROBOTIC INSPECTION OF SEWER PIPELINES

Section 33 01 30.18 – ACOUSTIC SENSOR IN-LINE DAMAGE DETECTION

Section 33 01 30.52 – HYDRAULIC SEWER CLEANING

Section 33 01 30.53 – SANITARY SEWER POINT REPAIRS BY CHEMICAL GROUTING

Section 33 01 30.63 – MANHOLE MAINTENANCE

1.03	SUBMITTALS

- Health and Safety Program – Document the CONTRACTOR’S Health and Safety Program for inclusion in the Planning Document. The Health and Safety Program shall include, but not be limited to, the safety policies needed to prevent damage, injury, or loss to all persons on the work site or who may be affected by the work.

- OSHA DART and TRC Ratings – Incorporate written certification of the CONTRACTOR’S OSHA DART and TRC ratings for the past three years into the Health and Safety Program.

- Hot Work Permit – Submit the Hot Work Permit upon completion of the work.

- Confined Space Entry Permit(Form CS-2) – Submit Form CS-2 upon cancellation of the permit.

1.04	APPLICABLE PUBLICATIONS

- Western Lake Superior Sanitary District Confined Space Entry Policy.

- Western Lake Superior Sanitary District Hazardous Energy Control Procedure.

1.05	STANDARDS AND CERTIFICATIONS

A.	The following standards shall be followed while executing the work required by the Contract Documents:

1.	Safety and Health Regulations for Construction, promulgated by the Secretary of Labor under Section 107 of the Contract Work Hours and Safety Standards Act, as set forth in Title 29, C.F.R.  Copies of these regulations may be obtained from Labor Building, 14th and Constitution Avenue N.W., Washington, DC 20013.

2.	Federal Occupational Safety and Health Act, as amended.

1.06	QUALITY ASSURANCE (NOT USED)

1.07	QUALIFICATIONS (NOT USED)

PART 2	PRODUCTS (NOT USED)

PART 3	EXECUTION

3.01	DOCUMENTATION AND NOTIFICATION

A.	Safety Program – Document the Health and Safety Program for incorporation in the Planning Document according to the requirements of  Paragraph 1.03 of this Section and Section 01 33 00 – SUBMITTALS.

- Notification of Start of Work – Contact Process Control to notify the operator that the CONTRACTOR will be on site completing the work required in the Contract Documents before starting the Field Work as defined in Section 01 11 00 – SUMMARY OF WORK.  Process Control can be contacted at the following phone number: (218) 740-4801 (or extension #301 from in plant phones).

- No Smoking Policy – Notify employees that smoking is not permitted on District property.

- Personnel List – Maintain a list of personnel working on the site. The list should include documentation that each person has been trained according to the CONTRACTOR’S Safety Program and has read and understands the requirements of this Section.

- Notification of Confined Space Entry – Notify the Field Representative prior to a confined space entry.

F.	Notification of Accident – Notify the Field Representative of any and all accidents or incidents on the work site or pertaining to the work which have caused an injury.

G.	Hot Work Permit – Obtain and complete a Hot Work Permit for electric or gas welding, cutting, brazing, or similar flame or spark producing operations that will be conducted anywhere in District facilities or on District property.

3.02	GENERAL

A.	Designate a site Safety Representative that will be available at all times while the work is in progress.

- When a conflict exists between the CONTRACTOR’S Safety Program policies and the Contract Documents, follow the most stringent requirement.

- Assume full responsibility for injuries to persons and for damages to property and services of the District, and for claims, losses or expenses which may in any way arise out of or result from the CONTRACTOR’S performance of this contract unless caused by the negligence or willful misconduct of the District’s agents, or employees. Indemnify and save the District harmless from such claims, losses or suits for injuries, death or damage and from liens, losses, expenses or claims of any sort arising therefrom and defend on behalf of the District any suit brought against the District for any such damage, injury or death. Reimburse the District for attorneys’ fees and for other expenses incurred by the District in connection with or as a result of any such suit.

- Do not use District equipment unless otherwise specified.

3.03	SAFETY AND HYGIENIC PRECAUTIONS

- Hygienic Precautions – Require personnel working on the District’s collection facilities to observe proper hygienic precautions including washing properly, and not eating or smoking except after washing hands as personnel could be exposed to wastewater containing disease-producing organisms.

B.  Safety Precautions – Take measures to make sure that personnel observe proper safety precautions when working on the District’s collection facilities. Solvents, gasoline, and other hazardous materials enter the pump stations and conveyance system with incoming sewage, and therefore, certain areas are hazardous to open flame, sparks, or unventilated occupancy. The District’s collection facilities can be extremely hazardous in terms of potential accident-causing situations.

C.  Protective Clothing and Equipment – Require personnel working on District property to wear safety glasses, steel toed shoes, and hard hats at all times. Require personnel working on District property in areas where they could be exposed to wastewater or residuals to wear proper protective equipment including: gloves, masks, eye protection, and protective body clothing.

3.04	CONFINED SPACE ENTRY

A.	Confined Space Entry requirements in accordance with OSHA 1910.146, MN Rule 5207.0300 through 5207.0310 and the WLSSD Confined Space Entry Policy shall be followed anytime CONTRACTOR’S personnel are in a confined space as defined by OSHA 1910.146.

# All manholes, pipelines, wet wells and other permitted confined spaces which contain or have contained wastewater may not contain enough oxygen to support life. Atmosphere in these areas shall be monitored and ventilated prior to and during entry.

- CONTRACTOR shall follow the WLSSD Confined Space Entry Policy and use the WLSSD Confined Space Entry Permit (Form CS-2 for all entries into permitted confined spaces).

3.05	HOT WORK PERMIT

A.	Obtain and complete a Hot Work Permit before conducting hot work activities. There are special procedures that are to be followed for hot work that is to be conducted in a confined space. These procedures are outlined in the District’s Confined Space Entry policy which should be reviewed before attempting entry (also refer to lockout/tag-out procedures), and include:

- All necessary work and emergency equipment shall be gathered prior to entry.

- After calibration of monitor, the area shall be tested prior to entry by trained personnel.

- Before any work begins, set up and start adequate ventilation equipment.

- A water hose of minimum 5/8” dia. shall be at the site, and shall be used to wet down all areas within the confined space.

- Close all mud valves and other ports of potential hazards.

- DO NOT do any digging of sand, gravel, or other debris as it may produce dangerous atmospheres.

- Before performing hot work, retest the air throughout the confined space, and at the point where the work is to be performed.

- Conduct continuous monitoring of the confined space.

- Maintain wet surfaces throughout the confined space.

- Open flames are to be used only for welding, cutting, brazing, etc. DO NOT use open flames for cleaning debris off surfaces, or other non hot work procedures.

B.	The Disctict’s Hot Work Permit form is attached to this Section. Complete a permit for each hot work activity that is conducted as part of the Contract Documents. Keep the permit on file at the location of the hot work, until the hot work is completed. Submit the permit to the Field Representative upon completion of the hot work or expiration of the permit.

PART 4	MEASUREMENT AND PAYMENT

4.01	GENERAL

A.	The cost of safety and health requirements is incidental to the Work.

END SECTION

WLSSD Hot Work Permit

Date of Hot Work: ____/____/____ - to - ____/____/____ Start Time ________Finish Time ________

Hot work performed by WLSSD Employee  Contractor

Building/Location _____________________________________________________

Name of Hot Work Operator ____________________Name of Fire Watch (Area)___________________

(Above) ______________________________		(Below)________________________________

Work being performed _____________________________________________________________________________________

_____________________________________________________________________________________

Do not take Fire Alarms out of service unless it is the only option available

In case of Emergency Call 911

IMPORTANT

I verify that the precautions listed below are completed.

____________________________________________________________________________________

Signature of Employee performing Hot Work	Signature of Employee(s) performing Fire Watch

Prevent Fires

Check the applicable boxes:

General Fire Safety Precautions

Inspection of flame or spark-producing equipment is complete and found in good repair.

 Provide an ample amount of portable extinguishing equipment, i.e., as hand hose or extinguisher.

 Confine the work to the area specified on this permit.

Within 35 feet of Work Area

 No combustible fibers, dusts, vapors, or gases of liquids are in the area. Purge tanks and equipment previously containing such materials. Verify absence of gases or vapors by combustible gas detection instrument. Continuous monitoring of the area when there is a possibility of a leak developing in nearby piping, equipment or tanks.

 All floor and wall openings have been tightly covered.

 Sweep clean the surrounding floors, and if combustible, wet down (use shock protection when needed).

 Relocate all combustibles to greater than 35 feet from the operation and the remainder protected with metal guards or flame proofed curtains or covers (not ordinary tarpaulins).

Fire Watch

 Personnel assigned to watch for dangerous sparks in work area, including the floors above and below, during lunch or rest period, and a minimum of 30 minutes after completion of the work.

Confined Space and LO/TO

 Confined Space Entry required. (Refer to the WLSSD Confined Space Entry program for further procedures.) Permit available on the Intranet:

 Lockout/Tagout procedures needed; follow the District Hazardous Energy Control Procedure.